## Slide 1: MDVR Vulnerability Test
Telnet port scan using zenmap.
Find device ip using ifconfig.
List device etc/ directory with password file hash location.
Crack password using john.exe
Login to device through telnet.

## Slide 2: Tools Used To Exploit The MDVR
Putty (Telnet Client) link
Zenmap (Port Sniffer) link
John (MD5 Hash Cracker) link
CMSv6 (MDVR Application) link
BusPirate (Hardware UART Serial) link
Sublime 3 (Text Editor) link

## Slide 3: Bus Pirate Setup
Purchase the bus pirate from a local vendor.
Test the Bus Pirate UART protocol.
Connect The Bus Pirate.

## Slide 4: Bus Pirate Setup
I bought my Bus Pirate from a local vendor called Communica link

## Slide 5: Bus Pirate Setup
The MDVR device uses a Hi 3520 DRQCV200 H.264 codec processor.
This chip uses a UART serial however there is no headers to program so small tracks had to have wires soldered.
Tx, RX and GND connected.

## Slide 6: Bus Pirate Setup
After soldering the Bus Pirate had to be connected to the computer and accessed using putty’s serial mode.
Next the Bus Pirate had to be put into UART serial mode.

## Slide 7: Bus Pirate Setup
Now the power can be connected to the MDVR device and the terminal will receive information from the chip.

## Slide 8: CMSv6 Information Gathering
Send parameter to the device to retrieve the devices encrypted password.
User will have to have the privilege to send the device a parameter text and have a FTP server setup.
Also this can be extracted from the firmware .

## Slide 9: Find Device IP Configuration
The devices IP can be found by sending it a parameter using the command busybox ifconfig
The parameter gets executed in the same way that the password was extracted.

## Slide 10: Crack Hash With John
With the device hash in hand John can be used to crack the hash.
I used John the Ripper 1.8.0-jumbo-1 and it took a few mins.

## Slide 11: Zenmap Port Sniffer
Zenmap is used to find any open ports on the provided IP address.
Command sent Nmap –T4 –A –v 192.168.118.126

## Slide 12: Login Via Telnet
User= root
Password= 311010